## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
VHDL is a widely used design language.
VHDL is a structured language for logic design.
In this Module we will introduce the VHDL language so that you can begin to design logic circuits.
An Introduction to VHDL

## Slide 3
Copyright © 2019 University of Colorado
VHDL is a structured language, and can be easier than Verilog to learn as your first Hardware Description Language.
Since VHDL is language based, designs created earlier can be re-used.
Why learn VHDL?

## Slide 4
Copyright © 2019 University of Colorado
Like any new language
If you were going to learn Spanish :
Learn key phrases
Learn Grammar and Syntax
Make more complex sentences
Practice, Practice, Practice
How can you learn VHDL?

## Slide 5
Copyright © 2019 University of Colorado
A 4-bit Comparator
How would you write the VHDL code?
Result
A
B

## Slide 6
Copyright © 2019 University of Colorado
Why Learn VHDL (this video)
FPGA Design Flow
Intro to VHDL : Finite State Machine
How to speak VHDL, First phrases
VHDL Assignments, Operators, Types
VHDL Rules and Syntax, Interface Ports
Using VHDL in ModelSim : Download and Install
Using VHDL in Modelsim : Adding to your Toolkit
Videos in this Module

## Slide 7
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 8
Copyright © 2019 University of Colorado
Acquire proficiency designing digital circuits with Field Programmable Gate Arrays (FPGA)s
Employ industry-standard tools to design and implement programmable logic solutions using several Hardware Description Language (HDL) design entry methods, including VHDL, Verilog and System Verilog
Build proficiency by designing basic digital programmable logic circuits in VHDL, Verilog and System Verilog
Objectives

## Slide 9
Copyright © 2019 University of Colorado
Recap: FPGA Design Flow
Design Entry: Schematic or HDL
Functional Simulation
Synthesis or Mapping
Place and Route or Fitting
Timing Analysis and Simulation
Programming the Device
Test and Integration
Release

## Slide 10
Copyright © 2019 University of Colorado
FPGA Design Flow: Design Entry
Design Entry: Schematic or HDL
Functional Simulation
Synthesis or Mapping
Place and Route or Fitting
Timing Analysis and Simulation
Programming the Device
Test and Integration
Release

## Slide 11
Copyright © 2019 University of Colorado
FPGA Design Entry Methodologies
Logical correlation between schematic design entry and circuit implementation
Not always transferrable between different FPGA tools and technologies
Difficult to scale for larger designs
Schematic Entry

## Slide 12
Copyright © 2019 University of Colorado
FPGA Design Entry Methodologies
Hardware Description Languages (HDLs)
  VHDL
  Verilog
  System Verilog

## Slide 13
Copyright © 2019 University of Colorado
HDL Key Concepts
Describing a hardware circuit implementation that your tool chain will eventually interpret and synthesize into FPGA logic cells
HDL is concurrent, not sequential
FPGA logic cells are hardware; inherently executes in parallel
CPU code is software; inherently executes in sequence

## Slide 14
Copyright © 2019 University of Colorado
Review the FPGA design flow
Explore FPGA design entry options
Introduce key concepts of using Hardware Description Languages (HDLs) to describe circuit implementations
Summary

## Slide 15
Copyright © 2019 University of Colorado
Establish motivation for learning VHDL
Introduction to VHDL coding
Reinforce key concepts
Objectives

## Slide 16
Copyright © 2019 University of Colorado
Earn a great income writing VHDL for FPGA and ASIC devices
VHDL is more structured than Verilog and faster than schematic capture!
Learn a new language for efficient and reusable problem solving
Why Learn VHDL?

## Slide 17
Copyright © 2019 University of Colorado
[Video Title]
Describing a hardware circuit that will synthesize into FPGA logic cells or gates
Logic is concurrent, not sequential
  FPGA gates are hardware; executes in parallel
  CPU code is software; executes serially
HDL Key Concepts
References: https://en.wikipedia.org/wiki/Field-programmable_gate_array

## Slide 18
Copyright © 2019 University of Colorado
Finite State Machine Example
State encoding
  S(Q1, Q0) = “00”, “10”
State table
INPUT : Reset, Run, Clk
OUTPUT : R Result
STATE : Current, Next
S0
---
R=0
S1
---
R=1
Reset
Run
Run
Reset
Run
Run
Current State |  | IN | Next State |  | OUT
Q1 | Q0 | Run | D1 | D0 | R
0 | 0 | 0 1 | 0 0 | 1 1 | 0 0
0 | 1 | 0 1 | 0 1 | 1 0 | 0 1
1 | 0 | 0 1 | 1 0 | 0 1 | 1 0
1 | 1 | 0 1 | 0 0 | 1 1 | 0 0

## Slide 19
Copyright © 2019 University of Colorado
Finite State Machine Example
Current State |  | IN | Next State |  | OUT
Q1 | Q0 | Run | D1 | D0 | R
0 | 0 | 0 1 | 0 0 | 1 1 | 0 0
0 | 1 | 0 1 | 0 1 | 1 0 | 0 1
1 | 0 | 0 1 | 1 0 | 0 1 | 1 0
1 | 1 | 0 1 | 0 0 | 1 1 | 0 0

## Slide 20
Copyright © 2019 University of Colorado
Finite State Machine Example
S0
---
R=0
S1
---
R=1
Reset
Run
Run
Reset
Run
Run
VHDL Description

## Slide 21
Copyright © 2019 University of Colorado
[Video Title]
VHDL describes hardware implementations
A VHDL design consists of
  Entity : interface = input, output ports
  Architecture : implementation = design logic
Example: AND gate
Introduction to VHDL

## Slide 22
Copyright © 2019 University of Colorado
[Video Title]
Introduction to VHDL
-- (VHDL comment)
-- Import std_logic library
library IEEE;
use IEEE.std_logic_1164.all;
-- Entity
entity ANDGATE is
port ( A : in std_logic;
B : in std_logic;
Y : out std_logic);
end entity ANDGATE;
-- Architecture
architecture RTL of ANDGATE is
begin
Y <= A AND B;
end architecture RTL;

## Slide 23
Copyright © 2019 University of Colorado
[Video Title]
Example: Basic Logic
Introduction to VHDL
Y
E
C
A
B
D

## Slide 24
Copyright © 2019 University of Colorado
Introduction to VHDL
-- (VHDL comment)
-- Import std_logic library
library IEEE;
use IEEE.std_logic_1164.all;
-- Entity
entity BasicLogic is
port (
A : in std_logic;
B : in std_logic;
C : in std_logic;
Y : out std_logic);
end entity BasicLogic;
-- Architecture
architecture RTL of BasicLogic is
Signal D, E : std_logic;begin
D <= NOT C;
E <= A OR B;
Y <= D AND E;
end architecture RTL;

## Slide 25
Copyright © 2019 University of Colorado
VHDL is a structured language
  Entity and Architecture pairs
Gates synthesized into hardware operate concurrently and in parallel
Summary

## Slide 26
Copyright © 2019 University of Colorado
VHDL Assignments : signals and variables
Operators : add, multiply, and everybody shift to the left
Objectives

## Slide 27
Copyright © 2019 University of Colorado
  Signals
    Signal wire to the entity : std_logic
    Scheduled update
    <= signal assignment operator
    Z <= A and B; -- concurrent, gates silicon
    Z <= D after 5ns; -- sequential, simulation
  Variables
    Variable only within the process : integer
    Immediate update
    := variable assignment operator
    count := count +1; --simulation loop counter
    a := 27; -- variable assignment
VHDL Assignments

## Slide 28
Copyright © 2019 University of Colorado
entity mux_4 is port(
a, b, c, d: in std_logic_vector(3 downto 0);
s: in std_logic_vector(1 downto 0);
x: out std_logic_vector(3 downto 0));
end mux_4;
architecture sel_arch of mux_4 is
begin
with s select
x <= a when “00”;
b when “01”;
c when “10”;
d when “11”;
d when others;
end sel_arch;
Select Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 29
Copyright © 2019 University of Colorado
architecture sel_arch of mux_4 is
begin
x <= a when ( s =“00”) else
b when ( s =“01”) else
c when ( s =“10”) else
d;
end sel_arch;
Conditional Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 30
Copyright © 2019 University of Colorado
architecture sel_arch of mux_4 is
begin
mux_proc: process(a, b, c, d, s)
begin
if s = “00” then x <= a;
elsif s = “01” then x <= b;
elsif s = “10” then x <= c;
else x <= d;
end if;
end process mux_proc;
end sel_arch;
Process Assignment
References: Kevin Skahill, VHDL for Programmable Logic.
Menlo Park, CA, Addison-Wesley, 1996, pp. 166

## Slide 31
Copyright © 2019 University of Colorado
[Video Title]
Operators
  ** exponent abs absolute value
  not complement + - add or subtract
  * multiply / divide
  mod modulo rem remainder
  sll, srl shift left, right
  rol, ror rotate left, right
  =, /=, <, <=, >, >= equality, greater, less than
  and, or, nand, nor, xor, xnor
Order precedence
  Left to right, Parenthesis
  Unary single operand on right mod A
  Binary operators on both sides A+B
VHDL Operators

## Slide 32
Copyright © 2019 University of Colorado
Array
  string “abc”
  bit_vector “1001”
  std_logic_vector “101Z”
Scalar
  character ‘a’
  bit ‘1’, ‘0’
  std_logic ‘1’, ‘0’, ‘X’, ‘Z’
  boolean true, false
  real, integer 3.14 1E+0, 27
  time fs, ps, ns, us, ms
Data Types – scalar and array types

## Slide 33
Copyright © 2019 University of Colorado
VHDL Assignments : signal and variable
  Logical Select
Operators - Dial 0
Scalar and Array data types
Summary