## Slide 1
Copyright © 2019 University of Colorado
[Instructor Name(s)]
[Department Name]
[Video Title]
FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
Copyright © 2019 University of Colorado
VHDL is a powerful and efficient language for logic design.
Now that the basics have been introduced, in this Module we will further explore how to use VHDL to design circuits through many examples and techniques.
An Introduction to VHDL

## Slide 3
Copyright © 2019 University of Colorado
Like learning any other language...
Learn key phrases, practice them
begun
Learn Grammar and Syntax
done
Make compound sentences
Practice, Practice, Practice
Learning to Speak VHDL

## Slide 4
Copyright © 2019 University of Colorado
Writing VHDL : A 4-bit Register
D
Q
En
R
D
Q
En
R
D
Q
En
R
D
Q
En
R
Clk
Load
Reset
D3
D2
D1
D0

## Slide 5
Copyright © 2019 University of Colorado
Writing VHDL : A 4-bit Register
-- Architecture
architecture Reg_Arch of Data_Reg is
begin dreg_proc : process (clk, reset, load)
begin
if (reset='0') then q <= "0000";
elsif (rising_edge(clk)) then
if (load='1') then q <= d;
end if;
end if;
end process dreg_proc;
end architecture Reg_Arch;a

## Slide 6
Copyright © 2019 University of Colorado
Learning to Speak VHDL (this video)
Combinatorial Circuits
Synchronous Logic: Latches and Flip Flops
Synchronous Logic: Counters and Registers
Interface: Buses and Tri-state Buffers
Modular Design in VHDL
Test Benches in VHDL - Combinatorial
Test Benches in VHDL – Synchronous
Memories in VHDL
Finite State Machines in VHDL
Videos in this VHDL Module

## Slide 7
Copyright © 2019 University of Colorado
In this video you will learn :
How to describe combinatorial circuits in VHDL
How to reduce vector sizes using reduction operators
Combinatorial Circuits in VHDL

## Slide 8
Copyright © 2019 University of Colorado
Basic Gate Assignments in VHDL
W
U
A
B
A
A
C
B
B
C
D
D
C
D
vA[0]
vA[1]
vB[0]
vA[2]
vA[3]
vB[2]
vB[1]
vB[3]
vX[1]
vX[2]
vX[3]
vX[0]
vB[3]
vY[3]
vA[3]
vA[2]
vA[1]
vA[0]
vB[0]
vB[1]
vB[2]
vY[2]
vY[1]
vY[0]
X
Y
Z

## Slide 9
Copyright © 2019 University of Colorado
Basic Gate Assignments in VHDL
-- Entity
entity gates is port (
vA, vB : in std_logic_vector(3 downto 0);
A,B,C,D : in std_logic;
W,U,X,Y,Z : out std_logic;
vX, vY : out std_logic_vector(3 downto 0) );
end entity gates;
-- Architecture
architecture RTL of gates is
begin
W <= A and B; U <= A nor B; --AND, NOR
X <= C xor D; Y <= C xnor D; --XOR, XNOR
Z <= (A and B) or (C and D); --AND-OR
vX <= vA and vB; -- Vector bitwise AND
vY <= vA or vB; -- Vector bitwise OR
end architecture RTL;

## Slide 10
Copyright © 2019 University of Colorado
Vector Reduction
in VHDL
-- Entity : Note: use IEEE.std_logic_misc.all;
entity gates is port (
vA, vB, vC, vD : in std_logic_vector(3 downto 0);
W,U,X,Y,Z : out std_logic );
end entity gates;
-- Architecture : reduction after VHDL-2008 tools
architecture RTL of gates is
begin
W <= AND_REDUCE(vA); -- Vector Reduction AND
U <= NOR_REDUCE(vB); -- Vector Reduction NOR
X <= XOR_REDUCE(vD); -- Vector Reduction XOR
Y <= OR_REDUCE(vA) and vB(0); -- OR Red, bit AND
Z <= OR_REDUCE(vA and vB); -- Bit AND, OR Red
end architecture RTL;

## Slide 11
Copyright © 2019 University of Colorado
Vector Reduction in VHDL
vA[2]
vA[3]
vB[1]
vB[2]
vB[3]
vA[0]
vA[1]
Z
vB[0]
W
U
vB[0]
vB[2]
vB[1]
vB[3]
vB[0]
Y
vA[0]
vA[1]
vA[2]
vA[3]
X
vD[2]
vD[1]
vD[3]
vD[0]
vA[0]
vA[1]
vA[2]
vA[3]

## Slide 12
Copyright © 2019 University of Colorado
Procedural Logic in VHDL
-- Entity
entity gates is port (
A,B,C,D : in std_logic;
Y : out std_logic );
end entity gates;
-- Architecture
architecture combo of gates is
begin combo_process : process (A,B,C,D)
begin
if ((C='1') and (D='1')) then Y <= '0';
elsif ((A='1') or (B='1')) then Y <= '1’;
else Y <= '0';
end if;
end process combo_process;
end architecture combo;

## Slide 13
Copyright © 2019 University of Colorado
Procedural Logic in VHDL - Circuit
A
B
C
D
Y

## Slide 14
Copyright © 2019 University of Colorado
Procedural Logic – Gotcha, Latch Generate
-- Entity
entity gates is port (
A,B,C,D : in std_logic;
Y : out std_logic );
end entity gates;
-- Architecture
architecture combo of gates is
begin combo_process : process (A,B,C,D)
begin
if ((C=‘1’) and (D=‘1’)) then Y <= ‘0’;
elsif ((A=‘1’) or (B=‘1’)) then Y <= ‘1’;
end if; -- Missing Else condition for Y
end process combo_process;
end architecture combo;

## Slide 15
Copyright © 2019 University of Colorado
Procedural Logic – Gotcha, Latch Generate
Incomplete Assignment
A
B
C
D
Y
Latch
D
C Q
R
‘1’

## Slide 16
Copyright © 2019 University of Colorado
In this video, you have learned:
How to describe combinatorial circuits in VHDL using either assignment statements
How to reduce vector sizes using operators as bus to bit reduction operators
How to prevent unintentional latches in logic circuits
Summary – VHDL for Combinatorial Circuits

## Slide 17
Copyright © 2019 University of Colorado
How can we make a D Latch in VHDL?
Synchronous Logic : D Latch
D
Q
GATE
CLR

## Slide 18
Copyright © 2019 University of Colorado
Synchronous Logic : D Latch
-- Entity
entity DLatches is port (
d, gate, clr : in std_logic;
q : out std_logic );
end entity DLatches;
-- Architecture
architecture LArch of DLatches is begin
latch_proc_1 : process (gate, d)
begin
if (gate='1') then q <= d;
-- No rising_edge()
end if;
-- No gate=0 value, so latch inferred
end process latch_proc_1;

## Slide 19
Copyright © 2019 University of Colorado
Synchronous Logic : D Latch
-- another Latch example
latch_proc_2 : process (gate, d, clr)
begin
if (clr ='1') then q <= '0';
elsif (gate='1') then q <= d;
end if;
end process latch_proc_2;
end architecture LArch;

## Slide 20
Copyright © 2019 University of Colorado
[Video Title]
Finite time for best case or worst case logic value to propagate a result through wires and logic cells across the chip
0 -> 1 transition for path C to Y
  0.2 + 0.9 + 0.3 + 1.1 + 0.2 = 2.7nano seconds
Combinatorial Logic
Y
E
C
A
B
D
0.2ns
0.9ns
0.3ns
1.1ns
0.2ns

## Slide 21
Copyright © 2019 University of Colorado
Logic path synchronized to CLK
Synchronous Logic
Y
E
C
A
B
D
D Q
CLK
Reset

## Slide 22
Copyright © 2019 University of Colorado
How can we make a D Flip Flop in VHDL?
Synchronous Logic : D Flip Flop
D
Q
R

## Slide 23
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Sync Reset
-- Entity
entity DFF is port (
d, clk, reset : in std_logic;
q : out std_logic );
end entity DFF;

## Slide 24
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Sync Reset
-- Architecture,
-- could use (clk'event and clk='1')
architecture DFF_Arch of DFF is
begin dff_proc_1 : process (clk)
begin
if (rising_edge(clk)) then
if (reset='1') then q <= '0';
-- Sync Reset
else q <= d;
end if;
end if;
end process dff_proc_1;
end architecture DFF_Arch;

## Slide 25
Copyright © 2019 University of Colorado
How can we make a D Flip Flop in VHDL?
Synchronous Logic : D Flip Flop – Async Reset
D
Q
R
S

## Slide 26
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Async Reset
-- Entity
entity DFF is port (
d, clk, set, reset : in std_logic;
q : out std_logic );
end entity DFF;
-- Architecture, Next Slide

## Slide 27
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Async Reset
-- Architecture
architecture DFF_Arch of DFF is
begin dff_proc_2 : process (clk, set, reset)
begin
if (reset='1') then q <= '0';
-- Async
elsif (rising_edge(clk)) then
if (set='0') then q <= '1';
-- Sync
else q <= d;
-- Sync
end if;
end if;
end process dff_proc_2;
end architecture DFF_Arch;

## Slide 28
Copyright © 2019 University of Colorado
How can we make a Clock Enable in VHDL?
Synchronous Logic : D Flip Flop
D
Q
R
En

## Slide 29
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Clock Enable
-- Entity
entity DFF is port (
d, clk, ce, reset : in std_logic;
q : out std_logic );
end entity DFF;
-- Architecture, Next Slide

## Slide 30
Copyright © 2019 University of Colorado
Synchronous Logic : D Flip Flop – Clock Enable
-- Architecture
architecture DFF_Arch of DFF is
begin dff_proc_3 : process (clk, ce, reset)
begin
if (reset='1') then q <= '0';
-- Async
elsif (rising_edge(clk)) then
if (ce='1') then q <= d;
-- Sync
end if;
end if;
end process dff_proc_3;
end architecture DFF_Arch;

## Slide 31
Copyright © 2019 University of Colorado
In this video, you have learned:
How to describe synchronous circuits in VHDL
How to design flip flops with synchronous and asynchronous set and reset
Summary – VHDL for Synchronous Circuits

## Slide 32
Copyright © 2019 University of Colorado
In this video you will learn :
How to describe synchronous circuits in VHDL
How to design registers and counters in VHDL
Synchronous Circuits in VHDL

## Slide 33
Copyright © 2019 University of Colorado
Data is stored in a register for later use. How can we make a data register in VHDL?
Synchronous Logic : Data Register
D
Q
En
R
D
Q
En
R
D
Q
En
R
D
Q
En
R
Clk
Load
Reset
D3
D2
D1
D0
Q3
Q2
Q1
Q0

## Slide 34
Copyright © 2019 University of Colorado
Synchronous Logic : Data Register
-- Entity
entity Data_Reg is port (
clk, reset, load : in std_logic;
d : in std_logic_vector(3 downto 0);
q : out std_logic_vector(3 downto 0));
end entity Data_Reg;
-- Architecture Next Slide

## Slide 35
Copyright © 2019 University of Colorado
Synchronous Logic : Data Register
-- Architecture
architecture Reg_Arch of Data_Reg is
begin dreg_proc : process (clk, reset, load)
begin
if (reset='0') then q <= "0000";
elsif (rising_edge(clk)) then
if (load='1') then q <= d;
end if;
end if;
end process dreg_proc;
end architecture Reg_Arch;a

## Slide 36
Copyright © 2019 University of Colorado
How can we make a shift register in VHDL?
D0 -> D1 -> D2 -> D3
Synchronous Logic : Shift Register
D
Q
En
R
D
Q
En
R
D
Q
En
R
D
Q
En
R
Clk
Shift
Reset
D0
Q0
Q1
Q2
Q3

## Slide 37
Copyright © 2019 University of Colorado
Synchronous Logic : Shift Register
-- Entity
entity Shift_Reg is port (
clk, reset, shift, d0 : in std_logic;
q : out std_logic_vector(3 downto 0));
end entity Shift_Reg;
-- Architecture Next Slide

## Slide 38
Copyright © 2019 University of Colorado
Synchronous Logic : Shift Register
-- Architecture, could SLL or shift_left(q,1)
architecture SREG_Arch of Data_Reg is begin
sreg_proc : process (clk, reset)
begin
if (reset='0') then q <= "0000";
elsif (rising_edge(clk)) then
if (shift='1') then
q(0) <= d0;
q(1) <= q(0);
q(2) <= q(1);
q(3) <= q(2);
end if;
end if;
end process sreg_proc;
end architecture SREG_Arch;

## Slide 39
Copyright © 2019 University of Colorado
How can we make a binary counter in VHDL?
Synchronous Logic : Binary Counter
Counter
Load
Data (D3..D0)
Clock
En
Q (D3..D0)
Reset

## Slide 40
Copyright © 2019 University of Colorado
Compile : Use ModelSim Library - 2008
Synchronous Logic : Binary Counter

## Slide 41
Copyright © 2019 University of Colorado
Synchronous Logic : Binary Counter
-- Entity
entity Counter is port (
clk, reset, load, en : in std_logic;
d : in std_logic_vector(3 downto 0);
q : out std_logic_vector(3 downto 0));
end entity Counter;
-- Architecture Next Slide

## Slide 42
Copyright © 2019 University of Colorado
Synchronous Logic : Binary Counter
-- Architecture
architecture Counter_Arch of Counter is begin
count_proc : process (clk, reset, load, en)
begin
if (reset='1') then q <= "0000";
elsif (rising_edge(clk)) then
if (load='1') then q <= d;
elsif (en='1') then q <= q + 1;
--2008
end if;
end if;
end process count_proc;
end architecture Counter_Arch;

## Slide 43
Copyright © 2019 University of Colorado
Register Files are useful constructs that allow addressing of registers. Each flop is assumed as an n-bit register.
Synchronous Logic : Register File
Clk
wdata
rdata
wAddress
wren
rAddress
D
Q
En
D
Q
En
D
Q
En
D
Q
En
Decoder

## Slide 44
Copyright © 2019 University of Colorado
Synchronous Logic : Register File
-- Entity -- use IEEE.numeric_std.all; integer conversion
entity regFile is
generic (Dwidth : integer := 8;
Awidth : integer := 2 );
port (
clk, wren : in std_logic;
wdata : in std_logic_vector(Dwidth-1 downto 0);
waddr, raddr : in std_logic_vector(Awidth-1 downto 0);
rdata : out std_logic_vector(Dwidth-1 downto 0) );
end entity regFile;
-- Architecture, Next Slide

## Slide 45
Copyright © 2019 University of Colorado
Synchronous Logic : Register File
-- Architecture
architecture RFile_Arch of regFile is
type array_type (0 to 2**Awidth-1) of std_logic_vector (Dwidth-1 downto 0);
signal array_reg : array_type;
begin rf_proc : process (clk, wren, wdata, waddr, raddr)
begin
if (rising_edge(clk)) then
if (wren='1') then
array_reg(to_integer(unsigned(waddr))) <= wdata;
end if;
rdata <= array_reg(to_integer(unsigned(raddr)));
end if;
end process rf_proc;
end architecture RFile_Arch;

## Slide 46
Copyright © 2019 University of Colorado
In this video, you have learned:
How to describe synchronous circuits :
  Data Register
  Shift Register
  Counter
  Register File
Summary – VHDL for Synchronous Circuits

## Slide 47
Copyright © 2019 University of Colorado
In this video you will learn :
How to make tri-state and bi-directional bus systems
How to join and separate buses
Bus Systems in VHDL

## Slide 48
Copyright © 2019 University of Colorado
External connections on FPGA pins are often in a group of related signals known as a bus.
The I/O structure of FPGAs often allow the bus to be tri-stated, so that multiple drivers can be attached to the IO at the same time, with only one driver active.
Tri-state Buses

## Slide 49
Copyright © 2019 University of Colorado
Tri-state in VHDL
-- Entity
entity y_tri is port (
OE : in std_logic;
Dout : in std_logic_vector(3 downto 0);
Pinout : out std_logic_vector(3 downto 0) );
end entity y_tri;
-- Architecture
architecture tri_arch of y_tri is
begin
Pinout <= Dout when (OE='1'),
(others => "ZZZZ") when others ;
end architecture tri_arch;

## Slide 50
Copyright © 2019 University of Colorado
When driving external tri-stated buses, som protocol should be used to assure that only one drive is active on the bus at a time.
VHDL code can define tri-state buses, but tri-state buses are typically not implemented inside of an FPGA but rather as a mux/multiplexer.
Tri-state Buses

## Slide 51
Copyright © 2019 University of Colorado
The I/O structure of the FPGA will also allow us to create Bi-directional buses, in which the external pin can be treated as either an input or an output, depending on the state of the enable signal.
Bi-directional Buses

## Slide 52
Copyright © 2019 University of Colorado
Bi-directional Buses in VHDL
-- Entity
entity bidir is port (
OE : in std_logic;
Dout : in std_logic_vector(3 downto 0);
Din : out std_logic_vector(3 downto 0);
IOpin : inout std_logic_vector(3 downto 0) );
end entity bidir;
-- Architecture, Next Slide

## Slide 53
Copyright © 2019 University of Colorado
Bi-directional Buses in VHDL
-- Architecture
architecture bidir_arch of bidir is
begin bi_proc : process (OE, Dout)
begin
Din <= IOpin;
if (OE='1') then IOpin <= Dout;
elsif (OE='0') then IOpin <= "ZZZZ";
else IOpin <= "XXXX";
end if;
end process bi_proc;
end architecture bidir_arch;

## Slide 54
Copyright © 2019 University of Colorado
VHDL includes the concatenation operator which allows buses to be combined. Splitting buses can be done using indexing.
Joining and Splitting Buses

## Slide 55
Copyright © 2019 University of Colorado
Joining Buses in VHDL
-- Entity
entity bus_js is port (
A : in std_logic_vector(4 downto 0);
B : in std_logic_vector(2 downto 0);
X, Y : out std_logic;
Dout : out std_logic_vector(5 downto 0) );
end entity bus_js;
-- Architecture
architecture js_arch of bus_js is
begin js_proc : process (A,B) begin
Dout <= (B(2) & B(1) & B(0) &
A(2) & A(1) & A(0));
X <= A(3);
Y <= A(4);
end process js_proc;
end architecture js_arch;

## Slide 56
Copyright © 2019 University of Colorado
In this video, you have learned:
How to make tri-state and bi-directional bus systems
How to join and separate buses
Summary – VHDL for Bus Systems

## Slide 57
Copyright © 2019 University of Colorado
In this video, you will learn:
How to build bigger designs using modular design techniques
Use of loops in VHDL
How to use Generate to make copies of circuits
Modular Design in VHDL

## Slide 58
Copyright © 2019 University of Colorado
Many tools are provided in VHDL to make modular designs, including :
Component Instantiation
Looping
Generate Blocks
Tasks and Functions
Modular Design in VHDL

## Slide 59
Copyright © 2019 University of Colorado
A modular design in VHDL at the architecture level oftentimes consists only of component instantiations, which is the fundamental way to build hierarchy in a design.
  architecture MY_HIER of MY_UPPER is
  component MY_LOWER_OR port (
  A,B : in std_logic;
  Z : out std_logic);
  end component;
  begin
  MY_INST_1 : MY_LOWER_OR port_map (
  A=>A_UP, B=>B_UP, Z=>Z_UP);
  MY_INST_N : ...
  end architecture MY_HIER;
Component Instantiation in VHDL

## Slide 60
Copyright © 2019 University of Colorado
architecture Add16_Arch of Add16 is
  component Add4 port (
  A,B : in std_logic_vector(3 downto 0);
  Cin : in std_logic; Cout : out std_logic);
  Sum : in std_logic_vector(3 downto 0) );
  end component;
  Begin
  Add4_u1 : Add4 port_map (
  A=> A(3 downto 0), B=>(3 downto 0), Z=> Cin(0), Sum(3 downto 0) );
  ...
  Add4_u4 : Add4 port_map (
  A=> A(15 downto 12), B=>(15 downto 12), Z=> Cin(3), Sum(15 downto 12) );
  end architecture Add16_Arch;
Component Instantiation in VHDL

## Slide 61
Copyright © 2019 University of Colorado
There are several looping constructs in VHDL, including :
while, for
The for loop statement is written and behaves just like it does in C, as is the while loop.
The while loop executes a statement or block of statements until a condition like less than or a when compare is equal to exit or wait.
Looping in VHDL

## Slide 62
Copyright © 2019 University of Colorado
Looping in VHDL
-- Architecture
architecture Loop_Arch of my_loop is begin
while (I <= 8) loop
if (B = '1') then
Z(I) <= A(I);
end if;
I := I + 1;
end loop;
end architecture Loop_Arch;a

## Slide 63
Copyright © 2019 University of Colorado
Although loops can be used to generate data or test patterns, a common use of loops for synthesis is replication of many identical circuits within generate blocks.
The generate … end generate block specifies now an object is to be repeated.
The index variable of a for loop sets the number of elements to generate.
Generate in VHDL

## Slide 64
Copyright © 2019 University of Colorado
Generate in VHDL
-- Architecture
architecture XorGen_Arch of XorGen is begin
Gen_proc : for i in 0 to 7 generate
xout(i) <= xin1(i) xor xin(2);
end generate Gen_proc;
end architecture XorGen_Arch;a

## Slide 65
Copyright © 2019 University of Colorado
In this video, you have learned:
How to build bigger designs using modular design techniques
Use of loops in VHDL
How to use for ... Generate to make copies of circuits
Summary - Modular Design in VHDL

## Slide 66
Copyright © 2019 University of Colorado
In this video you will learn :
The concept of using a VHDL program, called a testbench, to test another VHDL program (your code)
How to write simple testbenches
How to use loops to generate stimulus
How to use assertions to determine and report test results
Testbenches in VHDL

## Slide 67
Copyright © 2019 University of Colorado
A testbench is a program written in any language for the purposes of exercising and verifying the functional correctness of the hardware model as coded.
Also known as a test fixture or test harness.
A testbench is a powerful tool for generating test stimulus and test results
What is a Testbench?

## Slide 68
Copyright © 2019 University of Colorado
A testbench can have several functional sections, including:
  Top-level testbench declaration
  Stimulus, Response, and Component Signal declarations
  Component (Device Under Test) instantiations
  Test Monitor which logs results and reports mis-compares
Testbench Functional Sections

## Slide 69
Copyright © 2019 University of Colorado
Testbench Structure : Exercise the Core
LOG FILE :
Compare Expected
Count Mis-Compares
Pass/Fail
Testbench.VHD
Test Stimulus
Compare Results
Core.VHD
Device Under Test
Any Hierarchy
OUTPUT :
Div_CLK_OUT
Done_OUT
Data_B_OUT[31:0]
INPUT :
Clock_IN
Reset_IN
Data_A_IN[31:0]

## Slide 70
Copyright © 2019 University of Colorado
Adder Test Bench
-- Entity : no port list !
entity tb_adder is end entity tb_adder;
-- Architecture
architecture test_arch of tb_adder is
component Add4 port (
Data1,Data2 : in std_logic_vector(3 downto 0);
Cin : in std_logic;
Cout : out std_logic;
Sum : out std_logic_vector(3 downto 0) );
end component Add4;
signal a_tb, b_tb : std_logic_vector(3 downto 0); -- INPUT
signal Cin : std_logic; -- INPUT
signal Sum_tb : std_logic_vector(3 downto 0); -- OUTPUT
signal Cout_tb : std_logic; -- OUTPUT
signal expect : std_logic_vector(3 downto 0); --expected

## Slide 71
Copyright © 2019 University of Colorado
Adder Test Bench
begin
-- DUT Instantiation
DUT : Add4 port map (
Data1 => a_tb, Data2 => b_tb,
Cin => Cin, Cout => Cout_tb, Sum => Sum_tb);
-- Stimulus by hand drawn waves, poor coverage
stim_proc : process begin
wait for 0ns;
a_tb <= "0010"; b_tb <= "0010"; Cin <= '0'; expect <= "0100";
wait for 10ns;
a_tb <= "1111"; b_tb <= "0000"; Cin <= '1'; expect <= "0000";
wait for 10ns;
a_tb <= "0010"; b_tb <= "0100"; Cin <= '1'; expect <= "0111";
wait;
end process stim_proc;

## Slide 72
Copyright © 2019 University of Colorado
Adder Test Bench
-- Monitor, use ieee.std_logic_textio.all;
-- use std.textio.all;
txt_out : process (Sum_tb, Cout_tb)
variable str_o : line;
begin
write(str_o, string'(" a=")); write(str_o, a_tb);
write(str_o, string'(" b=")); write(str_o, b_tb);
write(str_o, string'(" cin=")); write(str_o, Cin);
write(str_o, string'(" sum=")); write(str_o, Sum_tb);
write(str_o, string'(" cout=")); write(str_o, Cout_tb);
write(str_o, string'(" expect=")); write(str_o, expect);
assert false report time'image(now) & str_o.all
severity note;
end process txt_out;
end architecture test_arch;

## Slide 73
Copyright © 2019 University of Colorado
Adder Test Bench => Text Output ModelSim
VSIM 10 > run
# ** Note: 0 ns a=UUUU b=UUUU cin=U sum=UUUU cout=U expect=UUUU
# Time: 0 ns Iteration: 0 Instance: /tb_adder
# ** Warning: There is an 'U'|'X'|'W'|'Z'|'-' in an arithmetic operand, the result will be 'X'(es).
# Time: 0 ns Iteration: 0 Instance: /tb_adder/DUT
# ** Warning: There is an 'U'|'X'|'W'|'Z'|'-' in an arithmetic operand, the result will be 'X'(es).
# Time: 0 ns Iteration: 0 Instance: /tb_adder/DUT
# ** Note: 0 ns a=0010 b=0010 cin=0 sum=XXXX cout=X expect=0100
# Time: 0 ns Iteration: 2 Instance: /tb_adder
# ** Note: 0 ns a=0010 b=0010 cin=0 sum=0100 cout=0 expect=0100
# Time: 0 ns Iteration: 4 Instance: /tb_adder
# ** Note: 10 ns a=1111 b=0000 cin=1 sum=0000 cout=1 expect=0000
# Time: 10 ns Iteration: 3 Instance: /tb_adder
# ** Note: 20 ns a=0010 b=0100 cin=1 sum=0111 cout=0 expect=0111
# Time: 20 ns Iteration: 3 Instance: /tb_adder
write(str_o, string'(" cout=")); write(str_o, Cout_tb);

## Slide 74
Copyright © 2019 University of Colorado
Adder Test Bench => Text Output ModelSim
(ModelSim : Time messages removed)
# ** Note: 0 ns a=0010 b=0010 cin=0 sum=XXXX cout=X expect=0100
# ** Note: 0 ns a=0010 b=0010 cin=0 sum=0100 cout=0 expect=0100
# ** Note: 10 ns a=1111 b=0000 cin=1 sum=0000 cout=1 expect=0000
# ** Note: 20 ns a=0010 b=0100 cin=1 sum=0111 cout=0 expect=0111

## Slide 75
Copyright © 2019 University of Colorado
Adder Test Bench => Wave Output ModelSim

## Slide 76
Copyright © 2019 University of Colorado
Adder Test Bench : Automation with Loops
-- Architecture : Generates coverage and expected stimulus
Loop_proc: process
variable i, j, k : integer;
begin
for i in 0 to 15 loop a_tb <= i;
for j in 0 to 15 loop b_tb <= j;
for k in 0 to 1 loop
Cin <= k;
wait for 10ns;
expect <= a_tb + b_tb + Cin;
end loop;
end loo;
end loop;
end process Loop_proc;
end architecture test_arch;

## Slide 77
Copyright © 2019 University of Colorado
Adder Test Bench : Waves for Loops

## Slide 78
Copyright © 2019 University of Colorado
Adder Test Bench : Self Checking
From the previous slide, Replace
expect <= a_tb + b_tb + Cin;
with
if (sum_tb /= a_tb + b_tb + Cin) then
write(str_o, string'(“Error - Sum”));
writeline(output, str_o);
wait;
end if;

## Slide 79
Copyright © 2019 University of Colorado
In this video, you have learned:
How to use loops to generate stimulus
How to use assertions to report test results
Summary – VHDL for Combinatorial Circuits

## Slide 80
Copyright © 2019 University of Colorado
Counter Test Bench
Counter DUT
Load
Data (D3..D0)
Clock
En
Q (D3..D0)
Reset
Clock generator
Reset Generator
Counter Test Process
Qexpected (D3..D0)
Compare

## Slide 81
Copyright © 2019 University of Colorado
Counter Test Bench
-- Testbench Entity : No port list
entity Counter_tb is end entity Counter_tb;
-- Testbench Architecture
architecture Counter_arch of Counter_tb is
component Counter port (
d : in std_logic_vector(3 downto 0);
clk, reset, load, en : in std_logic;
q : out std_logic_vector(3 downto 0));
end component Counter;
constant delay : integer := 10; -- wait
constant n : integer := 4; -- width counter
constant T : time := 20 ns; -- clock period
signal clock : std_logic := '0'; -- clock generator
signal reset : std_logic := '0'; -- reset generator

## Slide 82
Copyright © 2019 University of Colorado
Counter Test Bench
-- Architecture
signal data_tb : std_logic_vector(n-1 downto 0) :=
"0000";
signal load : std_logic := '0'; -- stimulus
signal en : std_logic := '0'; -- stimulus
signal q_tb : std_logic_vector(3 downto 0);
-- output
signal check : std_logic_vector(n-1 downto 0) :=
"0000"; -- compare to count

## Slide 83
Copyright © 2019 University of Colorado
Counter Test Bench
begin
-- DUT Instantiation
DUT : Counter port map (
d => data_tb,
clk => clock, reset => reset,
load => load, en => en,
q => q_tb );
clk_gen : process begin
clock <= '0';
wait for T/2; -- 10 nsec of 0
clock <= '1';
wait for T/2; -- 10 nsec of 1, for 20 nsec period
end process;
reset <= '1', '0' after 10 ns; -- 10 nsec

## Slide 84
Copyright © 2019 University of Colorado
Counter Test Bench
test_proc : process
variable line_o : line;
begin
wait until falling_edge(reset); -- wait for reset
wait until falling_edge(clock); -- wait for a clock
load <= '1'; en <= '0';
data_tb <= "1010";
wait until falling_edge(clock);
if (q_tb /= "1010") then
write(line_o, string'("Load fail "));
write(line_o, q_tb);
writeline(output, line_o);
end if;

## Slide 85
Copyright © 2019 University of Colorado
Counter Test Bench
check <= "1010";
load <= '0';
en <= '1';
wait for 1 ns;
for i in 1 to 2**n loop
check <= check + 1;
wait until falling_edge(clock);
if (q_tb /= check ) then
report "count fail at time count" &
time'image(now) & integer'image(i);
end if;
end loop;
wait;
end process test_proc;
end architecture Counter_arch;

## Slide 86
Copyright © 2019 University of Colorado
Counter Test Bench Waves

## Slide 87
Copyright © 2019 University of Colorado
Memories are a common element in most digital systems.
Earlier in this course we described a register file circuit, in which individual registers were enabled for access by decoding an address.
We will extend this to include RAM and ROM memories.
Memory in VHDL

## Slide 88
Copyright © 2019 University of Colorado
Synchronous Logic : Register File
Register Files are useful constructs that allow addressing of registers. Here we assume each flip flop represents an n-bit register.
Clk
wdata
rdata
wAddress
wren
rAddress
D
Q
En
D
Q
En
D
Q
En
Decoder
D
Q
En

## Slide 89
Copyright © 2019 University of Colorado
Dual Port RAM
-- Entity
entity DPRAM is
generic (D_Width : integer := 8;
A_Width : integer := 10 ); -- 2**10 = 1024
port (
clk, we : in std_logic;
d : in std_logic_vector(D_Width-1 downto 0);
w_add, r_add : in std_logic_vector(A_Width-1 downto 0);
q : out std_logic_vector(D_Width-1 downto 0) );
end entity DPRAM;
-- Architecture, Next Slide

## Slide 90
Copyright © 2019 University of Colorado
Dual Port RAM
architecture DPR_Arch of DPRAM is -- Architecture
type ram_type is array (0 to 2**A_Width-1) of
std_logic_vector (D_Width-1 downto 0);
impure function read_file(txt_file : in string) return ram_type is
file ram_file : text open read_mode is txt_file;
variable txt_line : line;
variable txt_bit : bit_vector(D_Width-1 downto 0);
variable txt_ram : ram_type;
begin for i in ram_type'range loop
readline(ram_file, txt_line);
read(txt_line, txt_bit);
txt_ram(i) := to_stdlogicvector(txt_bit);
end loop; return txt_ram;
end function;
https://www.fpga4student.com/2018/08/how-to-read-image-in-vhdl.html

## Slide 91
Copyright © 2019 University of Colorado
Dual Port RAM
-- Architecture
signal ram : ram_type := read_file("initialRAM.txt");
-- Read the ram text file from the function
signal data_reg : std_logic_vector (D_Width-1 downto 0);
begin ram_proc : process (clk)
begin
if (rising_edge(clk)) then
if (we='1') then
ram(to_integer(unsigned(w_add))) <= d;
data_reg <= ram(to_integer(unsigned(r_add))) ;
end if;
end if;
q <= data_reg ;
end process ram_proc;
end architecture DPR_Arch;
https://www.fpga4student.com/2018/08/how-to-read-image-in-vhdl.html

## Slide 92
Copyright © 2019 University of Colorado
Dual Port RAM
-- Short RAM Text File : address 0 to 7, 8 bits
00001111
11110000
10101010
01010101
00000000
11111111
00110011
11001100

## Slide 93
Copyright © 2019 University of Colorado
ROM Memory
entity ROM is -- Entity
generic (D_Width : integer := 8;
A_Width : integer := 3 ); -- 2**3 = 8 address
port (
clk : in std_logic;
addr : in std_logic_vector(A_Width-1 downto 0);
data : out std_logic_vector(D_Width-1 downto 0) );
end entity ROM;
architecture ROm_Arch of ROM is -- Architecture
signal rom_d, data_reg : std_logic_vector
(D_Width-1 downto 0);
signal addr_sel : std_logic_vector (2 downto 0);

## Slide 94
Copyright © 2019 University of Colorado
ROM Memory
begin
addr_sel <= addr;
rom_proc : process (clk) begin
data_reg <= rom_d;
end process rom_proc;
https://www.fpga4student.com/2018/08/how-to-read-image-in-vhdl.html

## Slide 95
Copyright © 2019 University of Colorado
ROM Memory
lookup_proc : process begin -- Lookup Table
case(addr_sel) is
when "000" => rom_d <= "10000000"; when "100" => rom_d <= "00000000";
when "001" => rom_d <= "10101010"; when "101" => rom_d <= "10011001";
when "010" => rom_d <= "01010101"; when "110" => rom_d <= "10000001";
when "011" => rom_d <= "10000011"; when "111" => rom_d <= "11110000";
when others => rom_d <= "00000000"; -- +700 cases possible, X, U
end case;
end process lookup_proc;
data <= data_reg;
end architecture ROM;
https://www.fpga4student.com/2018/08/how-to-read-image-in-vhdl.html

## Slide 96
Copyright © 2019 University of Colorado
ROM Memory : Wave Addr=h3

## Slide 97
Copyright © 2019 University of Colorado
In this video, you have learned:
How to create RAM and ROM memory devices
How to initialize a memory using an external text file as input
How to create a Look Up Table
Summary – RAM and ROM Memory in VHDL

## Slide 98
Copyright © 2019 University of Colorado
In this video you will learn :
The rationale for using Finite State Machines
How to create Finite State Machines
Criteria for determining which state encoding formats to use
VHDL Finite State Machines

## Slide 99
Copyright © 2019 University of Colorado
Finite State Machines (FSM) are a very important part of digital design
(and software design, too) !
The state machine concept provides a highly reliable, maintainable, and methodical way to design circuits that perform a sequence of operations with great predictability.
State machines are always in a known state. Good designs make use of FSMs.
Finite State Machines

## Slide 100
Copyright © 2019 University of Colorado
FSMs are categorized into 2 types : Moore or Mealy
Moore : output depends on the state
Mealy : output depends on inputs and the state
Finite State Machines
Clock
Inputs
Mealy
Outputs
Reset
Moore
Outputs
Next State Logic
(combinational)
Current State Register
(sequential)
Output Logic
(combinational)
Output Logic
(combinational)
Douglas J. Smith, pp. 197

## Slide 101
Copyright © 2019 University of Colorado
State Diagram and State Table
Douglas J. Smith, pp. 197
Current State | Next State | Next State | Next State | Output | Output
 | Input = Move CW | Input = Move CCW | Input = NoMove | Desired Position | PosError
An0 | An45 | An315 | An0 | Current State | DesPos - PhyPos
An45 | An90 | An0 | An45 | .. | ..
An90 | An135 | An45 | An90 | .. | ..
An135 | An180 | An90 | An135 | .. | ..
An180 | An225 | An135 | An180 | .. | ..
An225 | An270 | An180 | An225 | .. | ..
An270 | An315 | An225 | An270 | .. | ..
An315 | An0 | An270 | An315 | .. | ..
An270
An0
An180
An315
An225
An90
An45
An135
MoveCCW
NoMove
MoveCW

## Slide 102
Copyright © 2019 University of Colorado
State Encoding Types
No. | Binary | Gray | Johnson | One-Hot
0 | 000 | 000 | 0000 | 00000001
1 | 001 | 001 | 0001 | 00000010
2 | 010 | 011 | 0011 | 00000100
3 | 011 | 010 | 0111 | 00001000
4 | 100 | 110 | 1111 | 00010000
5 | 101 | 111 | 1110 | 00100000
6 | 110 | 101 | 1100 | 01000000
7 | 111 | 100 | 1000 | 10000000
Pong P. Chu, "Embedded SOPC Design with NIOS II Processor and Verilog Examples", pp. 100

## Slide 103
Copyright © 2019 University of Colorado
Binary Encoding
entity AngleFSM is -- Entity
generic (
S_Width : integer := 3; -- State Width
An0 : std_logic_vector(3 downto 0) := "000";
An45 : std_logic_vector(3 downto 0) := "001";
An90 : std_logic_vector(3 downto 0) := "010";
An135 : std_logic_vector(3 downto 0) := “011";
An180 : std_logic_vector(3 downto 0) := “100";
An225 : std_logic_vector(3 downto 0) := “101";
An270 : std_logic_vector(3 downto 0) := “110";
An315 : std_logic_vector(3 downto 0) := “111" );

## Slide 104
Copyright © 2019 University of Colorado
Binary Encoding
port (
clk, reset , MoveCw, MoveCCW : in std_logic;
PhyPosition : in std_logic_vector(S_Width-1 downto 0);
DesPosition, PosError : out
std_logic_vector(S_Width-1 downto 0));
end entity AngleFSM;
architecture FSM_Arch of AngleFSM is -- Architecture
signal CurrentState, NextState :
std_logic_vector (S_Width-1 downto 0);
begin

## Slide 105
Copyright © 2019 University of Colorado
Binary Encoding
comb_proc : process (MoveCw, MoveCCW, PhyPosition,
CurrentState)
begin
case(CurrentState) is
when An0 =>
if (MoveCW = '1') then NextState <= An45;
elsif (MoveCCW = '1') then NextState <= An315;
else NextState <= An0;
when An45 =>
if (MoveCW = '1') then NextState <= An90;
elsif (MoveCCW = '1') then NextState <= An0;
else NextState <= An45;

## Slide 106
Copyright © 2019 University of Colorado
Binary Encoding
-- ... Insert States An90 to An315 here
when An315 => -- Last State, others states
if (MoveCW = '1') then NextState <= An0;
elsif (MoveCCW = '1') then NextState <= An270;
else NextState <= An315;
when others => NextState <= An0;
end case;
end process comb_proc;
clk_proc : process (clk, reset) begin
if (reset = '1') then CurrentState <= PhyPosition;
elsif (rising_edge(clk)) then CurrentState <= NextState;
end process clk_proc;
end architecture FSM_Arch;

## Slide 107
Copyright © 2019 University of Colorado
Binary Encoding
-- Output Logic
-- Moore Output
DesPosition <= CurrentState;
-- Mealy Output
PosError <= DesPosition - Phy Position;
end architecture FSM_Arch;

## Slide 108
Copyright © 2019 University of Colorado
Binary Encoding - Schematic

## Slide 109
Copyright © 2019 University of Colorado
State Encoding - Compare Cell Usage
Encoding | Registers (FFs) | Total Logic Cells FSM | Output Encoding Conversion Logic | Total Logic Cells
Binary | 3 | 17 | 0 | 17
Gray | 3 | 20 | 9 | 29
Johnson | 4 | 36 | 9 | 51
One-Hot | 8 | 107 | 33 | 146

## Slide 110
Copyright © 2019 University of Colorado
In this video, you have learned:
The rationale for use of Finite State Machines
How to create Finite State Machines
Some criteria for determining which state encoding formats to use
Summary – Finite State Machines in VHDL