## Slide 1: FPGA Design for Embedded Systems
Hardware Description Languages for Logic Design

## Slide 2
An Introduction to Verilog
Verilog is one of the most popular, if not the most popular, languages for logic design.
In this Module we will introduce the Verilog language so that you can begin to design logic circuits with it.

## Slide 3
Why learn Verilog?
It’s fun.
You can make a living doing this.
It’s better than writing code in VHDL.

## Slide 4
How can you learn Verilog?
Like any other language…
If you were going to learn Spanish…
Learn key phrases, practice them
Learn Grammar and Syntax
Make compound sentences
Practice, Practice, Practice

## Slide 5
Writing Verilog for
A 4-bit Comparator

## Slide 6
Videos in this Module
Verilog for fun and profit
Your First Verilog Phrase
Verilog Rules and Syntax
Verilog Statements and Operators
Verilog Modules, Port Modes and Data Types
Verilog Structure
Testing Your Verilog with ModelSim: Download and Installation
Testing Your Verilog with ModelSim: Adding to Your Toolkit

## Slide 7
An Introduction to Verilog
In this video, you will learn:
The history of the Verilog HDL Language
An approach to learning Verilog
A “first phrase” design example (a comparator), done 3 different ways

## Slide 8
An Introduction to Verilog
Verilog, standardized as IEEE 1364, is a hardware description language (HDL) used to model electronic systems.
It is most commonly used in the design and verification of digital circuits at the register-transfer level of abstraction.
In Verilog, a design consists of modules.
A simple AND gate in Verilog would look something like the following:

## Slide 9
An Introduction to Verilog
// And gate
//
module andgate (x1, x2, f);
input x1, x2;
output f;
assign f = x1 & x2;
endmodule

## Slide 10
What is Verilog?
Verilog = Verifying Logic
Verilog - modeling language created by Gateway Automation in 1984.
Then to Cadence -> open standardization.
Now public domain -> Open Verilog International (OVI) (now known as Accellera) organization.
Verilog was later submitted to IEEE and became IEEE Standard 1364-1995, commonly referred to as Verilog-95.

## Slide 11
What is Verilog?
Extensions to Verilog-95 were submitted back to the IEEE. These extensions became IEEE Standard 1364-2001 known as Verilog-2001. Another update occurred in 2005.
As of 2009, the SystemVerilog and Verilog language standards were merged into SystemVerilog 2009 (IEEE Standard 1800-2009). The current version is IEEE standard 1800-2017.

## Slide 12
How can you learn Verilog?
Like any other language…
If you were going to learn Spanish…
Learn key phrases, practice them
Learn Grammar and Syntax
Make compound sentences
Practice, Practice, Practice

## Slide 13
Your first phrase in Verilog:
A 4-bit Comparator

## Slide 14
Three Modeling Styles in Verilog
Structural modeling (Gate-level)
Use predefined or user-defined primitive gates.
Dataflow modeling
Use assignment statements (assign)
Behavioral modeling
Use procedural assignment statements (always)

## Slide 15
Structural 4-bit Comparator
module comparator(
input[3:0] a,b, output out); // Verilog-2001 Syntax
wire n0, n1, n2, n3;
xnor xnor0( n0, a[0], b[0] );
xnor xnor1( n1, a[1], b[1] );
xnor xnor2( n2, a[2], b[2] );
xnor xnor3( n3, a[3], b[3] );
and and0( out, n0, n1,n2, n3 );
endmodule

## Slide 16
Dataflow 4-bit Comparator
module COMPARATOR
(A, B, Y); // Verilog-1995 Syntax
input [3:0] A, B,
output Y;
assign Y = & ( (A~^B));
endmodule

## Slide 17
Behavioral 4-bit Comparator
module COMPARATOR
(input [3:0] A, B;
output Y);
integer N;
reg Y;
always @(A or B)
begin: COMPARE
Y = 0;
if (A == B)
Y = 1;
end
endmodule

## Slide 18
Summary – Verilog Introduction
In this video, you have learned:
The history of the Verilog HDL Language from inception in 1984 until the latest IEEE revision in 2017
An approach to learning Verilog, involving assimilation of vocabulary, phrases and syntax
A “first phrase” design example (a comparator), modeled by use of structure, dataflow, or behavior.

## Slide 19
Verilog Fundamentals
Assignments
The fundamental statement in Verilog is the assignment statement. All assignment statements outside of an always block are concurrent – they happen at the same time, and are not sequential. The output of the operation on the right hand side of the = symbol is continuously assigned to the variable on the left hand side, as in
assign A = B & C; // an and gate
The variable on the LHS must be a net, not a reg when outside of an always block.

## Slide 20
Verilog Fundamentals
Assignments - Continuous
Assume we wanted to create this circuit:
How would this be coded in Verilog?
C
a
b
y

## Slide 21
Verilog Fundamentals
Assignments - Continuous
Answer: assign y = (a | b) & ~c;
Note that if we leave out the parens, we get:
assign y = a | b & ~c;
Because of the default order of evaluation.
C
a
b
y

## Slide 22
Verilog Fundamentals
Assignments – Procedural Procedural (blocking) assignments (=) are done sequentially in the order the statements are written. A second assignment is not started until the preceding one is complete. For example:
always @( posedge clk)
begin
Q2=Q1; Q1=D; // shift register
Q1=D; Q2=Q1; //single or parallel ff.
end

## Slide 23
Verilog Fundamentals
Assignments – nonblocking
RTL (nonblocking) assignments (<=), which follow each other in the code, are started in parallel. The right hand side of nonblocking assignments is evaluated starting from the completion of the last blocking assignment or if none, the start of the procedure. The transfer to the left hand side is made according to the delays. An intra-assignment delay in a nonblocking statement will not delay the start of any subsequent statement blocking or nonblocking.

## Slide 24
Verilog Fundamentals
Assignments – nonblocking
Using nonblocking statements, the intent of the previous example to create a shift register is preserved no matter the order.
always @( posedge clk)
begin
Q2<=Q1; Q1<=D; // shift register
Q1<=D; Q2<=Q1; // shift register
Q1<=D; Q2<=D; // parallel ff
end
Generally one would not code all 3 lines, but we are showing what would happen in each case.

## Slide 25
Verilog Fundamentals
Assignments – blocking/nonblocking
Guidelines
• One generally should not mix “<=” or “=” in the same procedure.
• “<=” best mimics what physical flip-flops do; use it only for “always @ (posedge clk ..) type procedures describing sequential circuits.
• “=” best corresponds to what c/c++ code would do; use it for combinational procedures, within or outside of always blocks.

## Slide 26
Verilog Operators
Operators, by precedence | Description
[ ] | bit-select or part-select
( ) | parenthesis, sets precedence order
! ,~ | Logical and bit-wise NOT
&, ¦, ~&, ~¦, ^, ~^, ^~ | Reduction AND, OR, NAND, NOR, XOR, XNOR; &(4’b0101) = 0 & 1 & 0 & 1 = 1’b0
+, - | unary sign, plus, minus; i.e. +18, -8
{ } | Concatenation: {3’b101, 3’b110} creates 6’b101110;
{{ }} | Replication; {3{3’b110}} creates 9’b110110110
*, /, % | Multiply, divide, modulus; Note: / and % may not be supported for synthesis
+, - | binary add, subtract.

## Slide 27
Verilog Operators
Operators, by precedence | Description (continued)
<<, >> | Shift left, shift right; X<<2 multiplies X by 4
<, <=, >, >= | comparison tests. Reg and wire variables are taken as positive numbers
==, != | logical equality test, logical inequality test
===, !== | case equality, case inequality; not synthesizable
& | bit-wise AND; AND together all the bits in a word If X=3’b101 and Y=3’b110, then X&Y = 3’b100, X^Y = 3b011
^, ~^, ^~ | bit-wise XOR, bit-wise XNOR
¦ | bit-wise OR;
&& | logical AND for use in decisions; Treats all variables as False(zero) or True(nonzero). (3&&0) is (T&&F) = 0
¦¦ | logical OR; (2¦¦-3) is (T¦¦T) = 1
?: | conditional, usually synthesizes to a mux. X = (cond)?T:F

## Slide 28
Verilog Fundamentals
How to make a Multiplexer
Assume we wanted to create this circuit:
How would this be coded in Verilog?
sel
a
b
y

## Slide 29
Verilog Fundamentals
How to make a Multiplexer
We could use a conditional assignment:
module mux(y, a, b, sel);
output y;
input a, b, sel;
assign y = sel ? a : b;
endmodule
The implementation would look something like this:
sel
a
b
y

## Slide 30
Verilog Fundamentals
How to make a Multiplexer
We could use gate primitives:
module mux(y, a, b, sel);
output y;
input a, b, sel;
and g1(y1, a, nsel),
g2(y2, b, sel);
or g3(y, y1, y2);
not g4(nsel, sel);
endmodule
sel
a
b
y
y1
y2
g3
g1
g2
g4
nsel

## Slide 31
Verilog Fundamentals
How to make a Multiplexer
We could use an always combinational block:
module mux(y, a, b, sel);
output y;
input a, b, sel;
reg y;
always @(a or b or sel)
if (sel) y = b;
else y = a;
endmodule
sel
a
b
y

## Slide 32
Verilog Fundamentals
How to make a Multiplexer
Lastly, we could use a User-Defined Primitive (UDP):
primitive mux(y, a, b, sel);
output y;
input a, b, sel;
table
1?0 : 1;
0?0 : 0;
?11 : 1;
?01 : 0;
11? : 1;
00? : 0;
endtable
endprimitive
sel
a
b
y

## Slide 33
Verilog Fundamentals
Ports
Input, Output, Inout - These keywords declare input, output and bidirectional ports of a module or task. Input and inout ports are of type wire. An output port can be configured to be of type wire, reg, wand, wor or tri. The default is wire.
module example(a, b, e, c)
input a; // An input, defaults to a wire
output b, e; // Outputs default to wire
output [1:0] c; /* 2-bit output, must be declared */
reg [1:0] c; // c port declared as reg

## Slide 34
Verilog Fundamentals
Buses
Suppose we have this Verilog code:
module invert(input [3:0] a, output [3:0] y);
assign y = ~a;
endmodule
What circuit would this produce? We’d get a bank of inverters, one for every bit between the 4-bit bus a and the 4-bit bus y. In a, the bits from most significant to least are a[3], a[2], a[1] and a[0] and can be accessed individually using this nomenclature. This is the little-endian order, because the least significant bit has the smallest bit number. If it had been written a[0:3], this would be big-endian order, with the MSB accessed with the smallest bit number.

## Slide 35
Verilog Fundamentals
Data Types – Nets and Registers
Nets
Represent connections between hardware elements
Must be driven continuously
Used to wire up instantiations
Include types wire, wor, tri and wand.
Registers
Retain the last value assigned
Often used to represent storage elements
Includes types reg and integer

## Slide 36
Verilog Fundamentals
Data Types
Integers are general-purpose variables.
For synthesis used mainly as loop indexes, parameters, and constants.
Implicitly of type reg, however they store data as signed numbers whereas explicitly declared reg types store them as unsigned.
If they hold numbers which are not defined at compile time, their size will default to 32-bits.
If they hold constants, the synthesizer adjusts them to the minimum width needed at compilation.

## Slide 37
Verilog Fundamentals
Data Types
Reg represents storage.
Only reg type variable can be assigned to in an always block.
Reg does not mean register. It can be modeled as a wire or as a storage cell depending on context. When used in combinational expressions in an always block, no storage is implemented. When used in sequential statements (begin/end, if, for, case, etc.), the a latch or FF will be created.

## Slide 38
Verilog Fundamentals
Port Rules
When connecting modules,
Inputs must be Nets (wire, etc.)
Outputs can be Nets or Registers
Inout must be Nets
The Left Hand Side (LHS) of procedural assignments must be of a Register type. For continuous assignments outside of procedural blocks, LHS must be Nets (wires).
These rules pictured visually on the next slide.

## Slide 39
Verilog Fundamentals
Port Rules
Module A
assign wire_out = … Net
always@(...)
reg_out <= … Reg
assign wire_inout = … Net
Module B
Net
Net
Net

## Slide 40
Verilog Fundamentals
Data Types
supply0 and supply1 define wires tied to logic 0 (ground) and logic 1 (power), respectively.
Time is a 64-bit quantity that can be used in conjunction with the $time system task to hold simulation time. Time is not supported for synthesis and hence is used only for simulation purposes.
Parameters allows constants like word length to be defined symbolically in one place. This makes it easy to change the word length later, by changing only the parameter.

## Slide 41
Verilog Fundamentals
Parameters and Buses
Assume we wanted to create this circuit:
How would this be coded in Verilog?
sel
a[0]
b[0]
outp[0]
a[1]
b[1]
outp[1]

## Slide 42
Verilog Fundamentals
Parameters and Buses
module bus_mux(a, b, sel, outp);
parameter n = 2;
input [n-1:0] a;
input [n-1:0] b;
input sel;
output outp;
wire [n-1:0] sel_bus;
assign sel_bus = {n{sel}}; //replicates 2 times
assign outp = (~sel_bus & a) | (sel_bus & b);
endmodule

## Slide 43
Verilog Structure
Modules
Modules are the basic building blocks in Verilog. A module definition always starts with the keyword module, followed by the module name, port list, port declarations, and parameters. This is followed in any order by:
Variable definitions (local scope)
Dataflow statements
Instantiation of lower modules
Behavioral Blocks
Tasks or Functions
Followed by the keyword endmodule (no semi-colon).

## Slide 44
Verilog Structure
module module_name (port_list);
endmodule
I. Port declarations
V. Module Instantiations
IV. Data Flow statements (assign …)
VI. Behavioral Blocks (begin…end)
VIII. Timing Specifications
II. Variable definitions
VII. Tasks or Functions
III. Parameters

## Slide 45
Verilog Structure
Module Instantiation
Modules can be instantiated by using ordered port lists, or by port names which don’t need to follow the module order. For example, here are 2 ways to instantiate a full adder:
reg [3:0] A, B; // top level signals in caps
reg C_IN;
wire [3:0] SUM;
wire C_OUT;
fulladd4 faordered(SUM, C_OUT, A, B, C_IN);
fulladd4 fa_name(.sum(SUM), .c_out(C_OUT),.a(A),.b(B), .cin(C_IN));

## Slide 46
Verilog Structure
Module Instantiation Gotcha
Modules can be instantiated by using ordered port lists, or by port names which don’t need to follow the module order. However, there is a possible gotcha when using the port list as seen here:
reg [3:0] A, B; // top level signals in caps
reg C_IN;
wire [3:0] SUM;
wire C_OUT;
fulladd4 faordered(C_OUT, SUM, A, B, C_IN);
fulladd4 fa_name(.c_out(C_OUT), .sum(SUM), .b(B), .cin(C_IN), .a(A));

## Slide 47
Verilog Structure
Making Bigger Circuits from Smaller
Recall the Verilog code for a 2-input mux:
module mux2(a, b, sel, y);
input [3:0] a, b;
input sel;
output [3:0] y;
assign y = sel ? b : a;
endmodule
How can we use this module to build a mux4?

## Slide 48
Verilog Structure
Making Bigger Circuits from Smaller
We can cascade the 2-input mux several times to make a 4-input mux :
module mux4(a, b, c, d, sel, y);
input [3:0] a, b, c, d;
input sel[1:0];
output [3:0] y;
wire[3:0] low, high;
mux2 lowmux(a, b, sel[0], low);
mux2 highmux(c, d, sel[0], high);
mux2 outmux(low, high, sel[1], y);
endmodule
We could have also made this by nesting conditional statements.

## Slide 49
Verilog Structure
module module_name (port_list);
endmodule
I. Port declarations and Parameters
V. Module Instantiations
IV. Data Flow statements (assign …)
VI. Behavioral Blocks (begin…end)
VII. Timing Specifications
II. Variable definitions
VII. Tasks or Functions
III. Parameters

## Slide 50
Example: Multiply-Accumulator
`timescale 1 ns/ 100 ps // time resolution/precis for sim
module mult_acc ( // module and name
input [7:0] data1, data2, // I. port declarations
input clk, aclr, // I. port declarations
output reg [15:0] mac_out ); // I. port declarations
wire [15:0] mult_out, add_out; // II. variable definition
parameter mult_size = 8; // III. parameter
assign add_out = mult_out + mac_out; // IV.dataflow
multiplr #(.width_in(mult_size)) // V. instantiation
u1 (.in_a(data1), .in_b(data2), .mult_out(mult_out));
always @ (posedge clk, posedge aclr) begin
if (aclr) // VI. behavioral block
mac_out <= 16'h0000;
else
mac_out <= adder_out;
end // end behavioral block
endmodule